## Slide 1: BIEE European Conference 2018
Prosumage of solar electricity: batteries, heating and mobility
Wolf-Peter Schill, Alexander Zerrahn, Michael Pahle
Oxford, September 18, 2018

## Slide 2: Overview
Introduction
The model
Input data
Results
(Preliminary) Conclusions and future research

## Slide 3: Introduction
Background: Our article in IAEE’s EEEP (2017)
  Qualitative discussion of prosumage from an economic perspective
  Quantitative illustration of selected system effects
  Focusing on battery storage and different operational strategies
  https://doi.org/10.5547/2160-5890.6.1.wsch
  Updated version forthcoming as a book chapter in „Energy Transition – Financing consumer (co-)ownership in renewables“, Lowitzsch, J. (Edt.), Palgrave Macmillan
  Extension: prosumage and sector coupling [work in progress]
  People may increase self-consumption also by electric heating or electric mobility
  We look at electric storage heaters and battery-electric vehicles
  Evaluation of system effects compared to batteries
1

## Slide 4: PRO-SUM-AGE und prosumagers
How we define PRO-SUM-AGE
  PROduction of renewable electricity (PV)
  ConSUMption of self-generated electricity
  StorAGE to temporally align supply and demand
Prosumagers
  produce their own renewable (PV) electricity at times,
  draw electricity from the grid at other times,
  feed electricity to the grid at other times,
  and make use of storage (stationary batteries, vehicle batteries, heat storage)
  Self-consumption vs self-generation
1
Source: own illustration

## Slide 5: Incentives for prosumage in Germany
Incentives for prosumage through FITs, LCOEs, and household tariffs
  Volumetric grid charges and EEG surcharge – but not on self-generation
  Strong decline of FIT compared to household tariff (“Socket parity“)
   We do not explicitly model this kind of incentive
1
Source: own illustration

## Slide 6: Pros and cons of prosumage from an economic perspective
Pros and cons depend on the perspective
  Prosumagers and other consumers
  Incumbent industry, new industry, service providers
  Electricity system / system operators
1
Arguments in favor of prosumage
Consumer preferences Lower/more stable electricity costs Participation/acceptance of energy transformation Activation of private capital Distribution grid relief
Arguments with ambiguous conclusions
Transmission grid relief Flexibility Driver for sector coupling Energy efficiency vs. rebound effect Local and macroeconomics benefits, increased competition Political economy, path dependency, and policy coordination Data protection and security
Arguments against prosumage
Increasing system costs Distributional impacts
 Further reading: EEEP article + book chapter

## Slide 7: A model-based analysis
Analysis with an extended version of the DIETER model
  Open-source electricity system model: www.diw.de/dieter
  Minimization of yearly system costs for dispatch and investment, hourly resolution
  Linear program, implemented in GAMS
  Exogenous inputs: cost and capacity data, time series on load and renewables
  Endogenous variables: costs, dispatch and investments
Representation of prosumage
  Some fraction of electric load and PV is assumed to engage in prosumage
  Varying (exogenous) minimum self-consumption restrictions
Options for increasing self-consumption
  Stationary Li-ion batteries
  Smart electric thermal storage (SETS)
  Battery-electric vehicles (BEV)
2

## Slide 8: Model extension: electric heating and electric mobility
2
Smart electric thermal storage (SETS)
Battery-electric vehicle

## Slide 9: Assumptions on different prosumage options
2
 | Electricity supply | Additional electricity demand | Investment cost | Other assumptions
Stationary li-ion batteries | Only self-generated | No (only losses) | 65 €/kW 300/kWh | E/P free No connection to grid
Smart electric thermal storage | Only self-generated | Yes | 350 €/kW (=44 €/kWh) | E/P 8 hours No connection to grid Natural gas back-up assumed Fluctuating heat demand profile (Horizon 2020 project)
Battery-electric vehicles | Self-generated and from grid | Yes | - (one BEV per household) | 3.7 kW / 30 kWh „Free lunch“ No V2G Time-varying charging availability profile (based on empirical German data)  available in 90% of hours

## Slide 10: Input data
Scenario for 2030 leaning on EU Reference Scenario
  ~53% renewables in electricity consumption
  25% of PV capacity attributed to prosumage segment, such that yearly PV generation = yearly load (w/o sector coupling)
  ~3.5 million prosumage systems with 4.6 kWp each
  Baseline self-consumption ~40-50%
  Endogenous investments in prosumage storage or SETS
  Further parameter assumptions
  System-average PV and load profiles also for prosumers
  No changes in generation portfolio
  No change in size of PV systems
3
Chart: 
| PV non-prosumage | PV prosumage | Wind offshore | Wind onshore | Bio | Other | Oil | OCGT | CCGT | Hard coal | Lignite | Run-of-river | PHS
 | 47.9695 | 15.9898 | 11.9315 | 55.2825 | 6.8943 | 0.17105 | 1.2481 | 13.489 | 13.489 | 21.8465 | 14.9284 | 5.8575 | 6.5
Installed capacity in GW

## Slide 11: Results: System costs, related to prosumager households
4
Chart: Self-consumption share
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Battery | 36.4646 | 101.9459 | 187.2118 | 8848.7922 | 25485.1602 | 57315.9643
Battery + SETS | 8.2813 | 20.2384 | 35.9168 | 80.2253 | 240.3737 | 6649.3834
Battery + SETS + BEV | 0 | 0 | 0.17276 | 9.1958 | 32.2242 | 675.6669
 Battery only: system costs increase strongly beyond 70% (log scale)
 Much lower costs if SETS are used, even more so if BEV are available
 What are the drivers?

## Slide 12: Results: Investments into storage (power) per prosumager household
4
Chart: kW per household
| Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | 50% | 60% | 70% | 80% | 90% | 100%
Li-ion | 0.51863 | 0 | 0 | 0.77308 | 0 | 0 | 1.1407 | 0 | 0 | 2.1388 | 0.32278 | 0 | 2.1388 | 1.0976 | 0 | 3.0314 | 2.8713 | 2.8713
SETS | 0 | 0.20413 | 0 | 0 | 0.53063 | 0 | 0 | 1.017 | 0 | 0 | 2.017 | 0.14187 | 0 | 1.8924 | 0.83451 | 0 | 3.108 | 0.65719
 Moderate investments in storage power (4 kWp PV) …

## Slide 13: Results: Investments into storage (energy) per prosumager household
4
Chart: kWh per household
| Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | 50% | 60% | 70% | 80% | 90% | 100%
Li-ion | 1.3277 | 0.0001 | 0 | 3.8165 | 0.0001 | 0 | 6.8694 | 0.0001 | 0 | 326.7737 | 0.61983 | 0.001 | 941.1736 | 6.8256 | 0.001 | 2116.2818 | 241.8378 | 21.8326
SETS | 0 | 1.6328 | 0 | 0 | 4.2445 | 0 | 0 | 8.135 | 0 | 0 | 16.1374 | 1.135 | 0 | 15.1399 | 6.676 | 0 | 24.8637 | 5.2576
 …but extreme investments into battery energy beyond 70%, “long-term storage”
 80-100%: much lower investments required if SETS (and BEV) are available
 Drivers: differences in investment costs, flexibility, and electricity demand
Notes: Extreme E/P ratio up to 700

## Slide 14: Results: Hourly storage charging level of stationary batteries (100% cases)
4
 Batteries only: seasonal smoothing of variable PV and load profiles
 If BEV are available: much more plausible short-term balancing
Chart: 

## Slide 15: Results: Shares of prosumagers‘ PV generation used for different options
4
Chart: 
| Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | 50% | 60% | 70% | 80% | 90% | 100%
To grid | 0.5 | 0.5 | 0.40753 | 0.4 | 0.4 | 0.36499 | 0.29999 | 0.3 | 0.3 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.1 | 0 | 0 | 0
Direct | 0.21306 | 0.42159 | 0.31574 | 0.19862 | 0.42153 | 0.33951 | 0.17535 | 0.42013 | 0.38677 | 0.10015 | 0.34663 | 0.40947 | 0.12507 | 0.29148 | 0.40616 | 0.061234 | 0.27126 | 0.33533
Li-ion | 0.28694 | 0 | 0 | 0.40138 | 0 | 0 | 0.52465 | 0 | 0 | 0.69985 | 0.10371 | 0 | 0.77493 | 0.39083 | 0 | 0.93877 | 0.48971 | 0.34067
SETS | 0 | 0.078406 | 0 | 0 | 0.17847 | 0 | 0 | 0.27987 | 0 | 0 | 0.34966 | 0.035654 | 0 | 0.21769 | 0.14113 | 0 | 0.23904 | 0.040274
BEV | 0 | 0 | 0.27673 | 0 | 0 | 0.2955 | 0 | 0 | 0.31323 | 0 | 0 | 0.35488 | 0 | 0 | 0.3527 | 0 | 0 | 0.28373
 Hardly any battery use if other options are available (except 100%)
 BEV crowd out SETS

## Slide 16: Sensitivity: 50% smaller PV installations System costs, related to prosumager households
4
 Higher “natural” self-consumption, much lower cost increases
 Smaller benefits of SETS and BEV
Chart: Self-consumption share
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Battery | 0 | 0 | 5.8739 | 75.5218 | 188.5826 | 1306.853
Battery + SETS | 0 | 0 | 1.442 | 15.7144 | 45.1274 | 581.1021
Battery + SETS + BEV | 0 | 0 | 0 | 0 | 0 | 425.6822

## Slide 17: Sensitivity: 50% smaller PV installations Investments into storage (energy) per prosumager household
4
 Much lower energy storage capacity required
Chart: kWh per household
| Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | 50% | 60% | 70% | 80% | 90% | 100%
Li-ion | 0 | 0.0001 | 0 | 0 | 0.0001 | 0 | 0.24073 | 0.0001 | 0 | 2.7973 | 0.001 | 0 | 7.123 | 0.001 | 0 | 48.3099 | 21.0521 | 15.4181
SETS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.35194 | 0 | 0 | 4.0567 | 0 | 0 | 12.6323 | 0 | 0 | 4.0892 | 0
Notes: Extreme E/P ratioup to 700

## Slide 18: Sensitivity: 50% smaller PV installations Shares of prosumagers‘ PV generation used for different options
4
 Larger role for direct use of PV electricity
 Less use of batteries and SETS
Chart: 
| Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | Battery | Battery + SETS | Battery + SETS + BEV | 50% | 60% | 70% | 80% | 90% | 100%
To grid | 0.5 | 0.5 | 0.43 | 0.34 | 0.4 | 0.25 | 0.3 | 0.3 | 0.16 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.1 | 0 | 0 | 0
Direct | 0.5 | 0.5 | 0.23 | 0.66 | 0.6 | 0.36 | 0.65 | 0.69 | 0.42 | 0.4 | 0.69 | 0.41 | 0.38 | 0.68 | 0.46 | 0.47 | 0.47 | 0.4
Li-ion | 0 | 0 | 0 | 0 | 0 | 0 | 0.05 | 0 | 0 | 0.4 | 0 | 0 | 0.52 | 0 | 0 | 0.53 | 0.52 | 0.41
SETS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01 | 0 | 0 | 0.11 | 0 | 0 | 0.22 | 0 | 0 | 0.01 | 0
BEV | 0 | 0 | 0.34 | 0 | 0 | 0.39 | 0 | 0 | 0.42 | 0 | 0 | 0.39 | 0 | 0 | 0.44 | 0 | 0 | 0.19

## Slide 19: Conclusions
Prosumage: a growing niche
  Growth depends on consumer attitudes, technology cost and regulatory framework
  Here: no assessment if prosumage is desirable or not
  Potential role of electric heating and electric mobility
  Batteries can increase self-consumption shares only to some extent
  SETS and BEV facilitate higher (cheaper) self-consumption shares
  Despite restrictions related to time profiles of heating and mobility demand
  (Preliminary) conclusions
  If households aim to achive higher self-consumption, increased sector coupling is likely (and desirable)
  Policy / regulation: avoid distortions at sector borders
5

## Slide 20: Future research
  Future research
  Exploration of different BEV profiles
  Other sector coupling options: hybrid / direct electric heating
  Further investigation of alternative PV sizing
  Impacts on overall generation portfolio, RES shares, and CO2 emissions
  Explicit consideration of regulatory environment
  Prosumage may help to unlock demand-side flexibility potentials  only „own“ electricity and no aggregator involved
  Complementary research: desirable amount of various sector coupling strategies in long-term decarbonization scenarios
5

## Slide 21
Wolf-Peter Schill wschill@diw.de

## Slide 22: Backup: distribution grid relief
Source: own illustration

## Slide 23: Backup: hourly heat demand profiles
Taken from European Horizon 2020 research project RealValue
Derived from dynamic simulations with RWTH building model
12 building archetypes; here we pick one-family houses with medium energy demand
Chart: Hours